| Activity / Task: Working at Height on Mobile Towers |
| --- |
| Persons at Risk: Employees, Volunteers |
| Additional Information | http://www.hse.gov.uk/construction/safetytopics/scaffold.htm |
| Hazard | Controls in Place | Severity of Harm S (1 to 5) | Likelihood of Harm L (1 to 5) | Risk Rating S x L = R | Additional Control Required |
| Injury due to: Falling from Height | Towers to be erected using the ‘through the trap’ method unless ‘advanced handrail’ system available Towers to be accessed using internal ladders / steps Do not use tower if any components missing or damaged Do not overload the tower Erect towers only on firm ground Only competent, trained (CPCS*, PASMA*), persons to erect towers Guard rails and toe boards to be fitted Do not attempt to climb out of the platform or stand on handrail Never extend the height of the platform by using a ladder, stepladder or hop-up | Without Controls |  |
|  |  | 5 | 4 | 20 HIGH |  |
|  |  | With all controls in place: |  |
|  |  | 3 | 2 | 6 LOW |  |

| Hazard | Controls in Place | Severity of Harm S (1 to 5) | Likelihood of Harm L (1 to 5) | Risk Rating S x L = R | Additional Control Required |
| --- | --- | --- | --- | --- | --- |
| Injury due to: Falling Objects | Persons working below towers to wear head protection Toe boards on working platform Working area around tower to be cordoned off | Without Controls |  |
|  |  | 4 | 1 | 4 LOW |  |
|  |  | With all controls in place: |  |
|  |  | 3 | 2 | 6 LOW |  |

| Hazard | Controls in Place | Severity of Harm S (1 to 5) | Likelihood of Harm L (1 to 5) | Risk Rating S x L = R | Additional Control Required |
| --- | --- | --- | --- | --- | --- |
| Injury due to: Tower scaffold falling | Operatives trained in erection, use and dismantling. Towers erected to manufactures instructions, out riggers used where indicated Weather conditions taken into consideration. The tower in a freestanding condition must be stable in wind speeds up to 28 mph (Beaufort 6). The tower must not be used if the wind speed is greater or equal to 17 mph. Brakes put on when used as a work platform No unauthorised adaptations Suitable barriers / warning signs to be placed around tower to worn passers-by / vehicle drivers | Without Controls | 10 Medium |  |
|  |  | 5 | 2 |  |  |
|  |  | With All Controls in Place | 5 LOW |  |
|  |  | 5 | 1 |  |  |

| Hazard | Controls in Place | Severity of Harm S (1 to 5) | Likelihood of Harm L (1 to 5) | Risk Rating S x L = R | Additional Control Required |
| --- | --- | --- | --- | --- | --- |
| Injury due to: Defective equipment | Equipment checked prior to use/ quarterly | Without Controls |  |
|  |  | 2 | 3 | 6 MEDIUM |  |
|  |  | With all controls in place: |  |
|  |  | 1 | 2 | 2 LOW |  |

| Hazard | Controls in Place | Severity of Harm S (1 to 5) | Likelihood of Harm L (1 to 5) | Risk Rating S x L = R | Additional Control Required |
| --- | --- | --- | --- | --- | --- |
| Injury due to: Electrocution | Do not erect or use near overhead power lines Be aware of overhead power lines when moving a tower | Without Controls |  |
|  |  | 2 | 3 | 6 MEDIUM |  |
|  |  | With all controls in place: |  |
|  |  | 1 | 2 | 2 LOW |  |

| Hazard | Controls in Place | Severity of Harm S (1 to 5) | Likelihood of Harm L (1 to 5) | Risk Rating S x L = R | Additional Control Required |
| --- | --- | --- | --- | --- | --- |
| Injury due to: Manual Handling | Manual handling assessment required Operatives trained in manual handling Mechanical handling where appropriate | Without Controls |  |
|  |  | 2 | 3 | 6 MEDIUM |  |
|  |  | With all controls in place: |  |
|  |  | 1 | 2 | 2 LOW |  |

| SEVERITY (CONSEQUENCE) |  | RISK / PRIORITY INICATOR MATRIX |
| --- | --- | --- |
| 1. Negligible (delay only) |  | LIKELIHOOD | 5 | 5 | 10 | 15 | 20 | 25 |
| 2. Slight (minor injury / damage / interruption) |  |  | 4 | 4 | 8 | 12 | 16 | 20 |
| 3. Moderate (Lost time injury, illness, damage, lost business) |  |  | 3 | 3 | 6 | 9 | 12 | 15 |
| 4. High (Major injury / damage, Lost time business interruption, disablement) |  |  | 2 | 2 | 4 | 6 | 8 | 10 |
| 5. Very High (Fatality / Business closure) |  |  | 1 | 1 | 2 | 3 | 4 | 5 |
|  |  |  | 1 | 2 | 3 | 4 | 5 |
| LIKELIHOOD |  |  | SEVERITY (CONSEQUENCE) |
| 1. Improbable / very unlikely |  |  |  |  |  |  |  |  |
| 2. Unlikely |  | SUMMARY | SUGGESTED TIMEFRAME |
| 3. Even chance / may happen |  | 12-25 | High | As soon as possible |
| 4. Likely |  | 6-11 | Medium | Within next 3-6 months |
| 5. Almost certain / imminent |  | 1-5 | Low | Whenever viable to do so |